PRESENTER'S GUIDE

"LADDER SAFETY"

Part of the "SAFETY MEETING KIT" Video Series

Quality Safety and Health Products, for Today...and Tomorrow

THE "SAFETY MEETING KIT"

VIDEO SERIES

This education program is part of the "Safety Meeting Kit" Video Series. The programs in this series have been created to provide employees with good, basic information on everyday safety and health topics. This series includes programs on the following topics:

- Accident Investigation

- The ANSI MSDS

- Back Safety

- Compressed Gas Cylinders

- Computer Workstation Safety

- Conflict Resolution (Industrial and Office versions)

- Crane Safety (Industrial and Construction versions)

- Driving Safety

- Dealing with Drug and Alcohol Abuse (Employees and Managers/Supervisors versions)

- Electrical Safety

- Eye Safety (Industrial and Construction versions)

- Ergonomics (Industrial and Office versions)

- Fall Protection

- Fire Extinguishers

- Fire Prevention (Healthcare, Industrial and Office versions)

- First Aid (Industrial and Construction versions)

- Hand and Power Tool Safety (Industrial and Construction versions)

- Hand, Wrist and Finger Safety (Industrial and Construction versions)

- Hazardous Materials Labels

- Hazardous Spill Cleanup

- Heat Stress (Industrial and Construction versions)

- Ladder Safety (Industrial and Construction versions)

- Machine Guard Safety

- Materials Handling Safety

- Office Safety

- Rigging Safety (Industrial and Construction versions)

- Safety Audits

- Safety Housekeeping and Accident Prevention

- Safety Orientation

- Safety Showers and Eye Washes

- Sexual Harassment (Employees & Managers/ Supervisors versions)

- Sexual Harassment Investigations

- Slips, Trips and Falls

- Welding Safety (Industrial and Construction versions)

- Wellness and Fitness

- Winter Safety

- Workplace Harassment (Industrial and Office versions)

- Workplace Stress

- Workplace Violence

Other products in the "Safety Meeting Kit" line include employee booklets and posters which have been designed specifically to be used with the programs. By combining these three products you have all of the materials you need to promote and conduct a complete safety meeting (for information on booklets and posters contact your local distributor)..

WARRANTY/DISCLAIMER

"This program has been created to assist companies that are endeavoring to educate their employees regarding good safety and health practices. The information contained in this program is the information available to the producers of the program at the time of its production. All information in this program should be reviewed for accuracy and appropriateness by companies using the program to assure that it conforms to their situation and recommended procedures, as well as to any state, federal or other laws, standards and regulations governing their operations. There is no warranty, expressed or implied, that the information in this program is accurate or appropriate for any particular company's environment."

Copyright 2010, The MARCOM Group, Ltd.

TABLE OF CONTENTS

Section

(	INTRODUCTION TO THE PROGRAM	 1

C	Structure and organization

C	Background

C	Objectives

C	Reviewing the program

(	PREPARING FOR THE PRESENTATION	 2

C	Structuring the presentation

C	Setting up the class and classroom

(	CONDUCTING THE SESSION	 3

C	The initial steps

C	Showing the program

C	Conducting the discussion

C	Concluding the presentation

C	"Wrapping up" the paperwork

(	OUTLINE OF MAJOR POINTS IN THE PROGRAM	 4

(	ACCOMPANYING MATERIALS	 5

C	Scheduling and Attendance Form

C	Quiz

C	Training Certificate

C	Employee Training Log

C	Booklet

INTRODUCTION TO THE PROGRAM

INTRODUCTION TO THE PROGRAM

Structure and Organization

Information in this program is presented in a definite order, so that employees will see the relationships between the various groups of information and can retain them more easily. The sections included in the program are:

Selecting the proper ladder.

Inspecting ladders before use.

Setting up and moving ladders.

Climbing ladders.

Working on ladders.

Ladder accidents.

Each of the sections covers important information in one topic area, providing employees with the basis for understanding the basics of ladder safety.

Background

Most of the time our days are spent with our feet firmly on the ground. At ground level, our tools and work surfaces are within easy reach. But there are times when we need access to things that are more difficult to get to.

Sometimes a truck with a "lift bucket" can be brought in to raise us to the desired height. For long-term projects, it may make sense to put up some scaffolding. Most of the time though, working off the ground means bringing in a ladder.

When we use them correctly, ladders make our jobs easier, and make us more productive. They allow us to work comfortably in places that are ordinarily out of our reach. In fact, it's hard to imagine what we'd do without them. But we've got to be careful, because whenever we're on a ladder there's always the possibility we could fall. If they're used incorrectly, ladders can lead to accidents and serious injuries.

This program will help employees to understand the basics of ladder safety and what you can do to help avoid accidents while working on a ladder.

Objectives

This education and training program reminds employees that while they may frequently work with ladders, they may not be aware of all of the problems that can occur with their use. The program reviews these potential problem situations with employees and instructs them on how to avoid or correct them. It also examines proper ladder use and climbing techniques, as well as what to do in case of a fall or other injury. Upon completion of the program, employees should be able to:

Properly transport and set up various types of ladders.

Recognize potential problems in working with ladders.

Take appropriate steps to avoid or counteract these problems.

Use proper techniques when climbing ladders.

Know how to handle tools and materials safely when using them with ladders.

Apply basic first aid to injuries that are caused by falls or other accidents when using ladders.

Reviewing the Program

As with any educational program, the "presenter" should go through the entire program at least once to become familiar with the content and make sure the program is consistent with company policy and directives.

An "Outline of Major Program Points" section is included in this Presenter's Guide to help with this task and for general reference.

As part of this review process, you should determine how you, as the presenter, will conduct your session. The use of materials such as handouts, charts, etc., that may be available to you needs to be well thought out and integrated into the overall program presentation.

PREPARING FOR THE PRESENTATION

PREPARING FOR THE PRESENTATION

Structuring the Presentation

In conducting this education session, you should proceed with a friendly and helpful attitude. Remember that the "trainees" are looking to your experience and knowledge to help them relate to the situations shown in the program. It is important to let the trainees interact with you and each other during the training session. Stimulating conversation within the group is one of the best things you, as the presenter of the program, can do to help everyone get as much as possible from the session. Be alert for comments that could help in this area in future sessions and make note of them.

As the presenter, you also should:

Keep the session related to the topic of ladder safety.

Relate discussions to how the knowledge of how to use ladders safely.

Keep any one person or small group of employees in the session from doing all the talking.

Get everyone involved. Ask questions of those who don't participate voluntarily.

Clarify comments by relating them to the key points in the program.

Use the "Outline of Major Program Points" section in this guide, as well as the information included in the quiz, as the basis for answering any questions. If you don't know the answer, say so. Tragic results may occur should you provide incorrect or inaccurate information. Remember, this is a positive program on ladder safety. Make sure your attitude and words reflect this and that the emphasis is always on providing the information needed by the attendees to improve their ability to work with ladders safely.

Setting Up the Class and Classroom

Remember, there are a number of things that must be done to "set up" the class as well as the classroom. These fall into several groups of activities, and include:

Scheduling and Notification

Use the enclosed form to schedule employees into the session.

Make sure that the session is scheduled so that it fits into your attendees' work day.

Send out notification of the session well in advance, to give people enough time to incorporate it into their schedule for that day.

If possible, post a notification on bulletin boards in the affected employees' areas.

The Classroom

Schedule the room well in advance.

Make sure the room can accommodate the expected number of attendees.

Check it again on the day of the program to make sure there is no conflict.

Make sure the room can be darkened, and won't create a glare on the television screen.

Locate the light controls and test them.

Make sure the power for the videotape or DVD player you are using operates separately from the room light.

See if you can control the room temperature.

Know where the closest restrooms are.

Assure that the room is free from distracting noises.

Make sure emergency exits are marked and known to the attendees.

Seating

Make sure everyone can see the screen from their seat.

Make sure everyone can hear the videotape/DVD and you (when you speak).

Check to see that seating is such that writing can be done easily.

Make sure the seating arrangement allows eye contact between attendees, and between you and attendees.

Equipment and Materials

Make sure a videotape or DVD player, monitor, and all appropriate cables and extension cords are available.

Make sure a stand or table is available and is of appropriate height for all attendees to easily see the monitor.

If you plan on using a chartpad, blackboard, or other writing board, make sure it is available, easy to see, and you have the proper writing implements.

Make sure you have 6" x 8" index cards or other materials to be used as "name tents" for attendees.

Make sure you have made up a sufficient number of copies of the quiz, as well as any other handouts you are using.

"Final Check"

Make sure equipment is in the room prior to the scheduled session.

Make sure you have the right program, (look inside the three-ring binder)!

Check to see that the room is set up properly.

Check equipment prior to the presentation to assure that it works.

Make sure extension cords, etc. are "taped down", if need be, to avoid tripping.

If you are using the videotape version of the program, run the "leader" up to the point where the program begins.

CONDUCTING THE SESSION

CONDUCTING THE SESSION

The Initial Steps

In conducting the session remember the positive nature of this presentation. Everyone is attending in order to learn more about ladder safety. Initially, you need to:

Introduce yourself as the session leader.

State the title of the program, "Ladder Safety" and the purpose of the session (to learn about using ladders safely).

Inform the attendees when there will be breaks (if you plan them), the location of exits and restrooms and if water, coffee, or other refreshments will be available.

Make sure all of the attendees have "signed in" on your scheduling and attendance sheet. Remember, it is very important to document peoples' attendance at the session.

Once this housekeeping is done, it is time to move to the "meat" of the session. First, the attendees need to be informed about the objectives of the session (this is where you can use a flip chart or board to list the objectives, which should be done prior to the class starting). This listing should be preceded with some introductory remarks. Your own words are always best, but the remarks should include information such as the following paragraphs:

"Today we are going to talk about ladder safety. There are many times when our jobs require that we have access to places that are higher than we can normally reach. A number of types of equipment can be used in these situations. When we are working with large amounts of material, or need a 'platform' to serve as our work surface, lift trucks can be very helpful, if they are available. For more permanent projects, scaffolding can be erected."

"However, in most situations we can use ladders to reach the areas that we need to work on. Ladders are easily transportable and can be set up quickly. They can make our jobs easier as well as make us more efficient. However, working with ladders can also be dangerous. Falling is always a potential problem. And there can be other hazards as well. Tools or materials dropped from ladder height can cause major damage and injury. Using metal ladders around electricity can cause shock and even electrocution."

"Avoiding these problems and hazard situations is possible. What we need to do is make sure we know how to use ladders properly and safely. The program we are going to watch today will give us some good information about ladder safety. We will learn how to transport and set up ladders correctly, how to recognize potential hazard situations, and the steps to take to avoid or correct them. To make this the most productive session possible we need to look at what we want to accomplish here today (verbally reference the 'Objectives' list from the first section, or gesture to a blackboard or chart where you have written them down)."

Once the objectives have been provided, you are ready to show the program. However, you do need to let the attendees know that they will be taking a quiz at the end of the session (if you are using it). It needs to be emphasized that they are not being "graded", but that the quiz is being used to see if the session is effectively transmitting information to them in a way they will remember.

Showing the Program

At this point, you need to introduce the title of the program once again, "Ladder Safety", darken the lights if necessary, and begin the showing of the program.

If you are using the DVD version of the course you have several options as to how you can move through the program and what employees see.

The DVD menu has three "selection bars":

"Play".

"Scene Index".

"Contact Info".

To just play the program from beginning to end, select "Play".

To view (or review) a specific section of the program, select "Scene Index". You will be presented with a group of buttons, each of which corresponds to a section of the program. You can then select the specific section that you want to view.

If you would like information on other programs and products that are available from MARCOM you can select "Contact Info" for information about how to contact us.

All of our DVDs, both English and Spanish, are subtitled (similar to closed captioning). If there are hearing impaired employees participating in your training session, or you want people to be able to read the program narration as well as hear it, push the "subtitle" button on your DVD player's remote control or the player's control panel. A print version of the narration will then appear on the bottom of the screen as the video plays.

Conducting the Discussion

After the program has been shown, it is time for the group discussion on the information contained in the session. Care must be taken to make sure that the discussion is kept to the general topic of ladder safety. There are several ways to conduct this discussion. These include:

Calling for questions from the attendees and using these questions as the basis for the discussion.

Leading the discussion through the points covered in the program using statements such as:

"One of the sections that we saw in the program was about using the proper set-up angle when positioning ladders. What is the correct angle for set-up and what are some ways to determine if you are using this angle?"

"We saw an interesting segment on proper ladder climbing techniques. Who can review these techniques for us, including the 'three-point' climb?"

You should use the discussion format that you are most comfortable with. The "Outline of Major Program Points" addressed in the program and the questions and answers in the master copies of the quiz can be very useful as a basis for discussion.

Remember, you have allocated a limited amount of time in which this discussion can take place. It is important to blend the attendees' questions and areas of obvious interest with the objective of trying to touch on each major area within the session in the discussion. By touching on each area, the attendees are much more likely to retain the information presented in the session.

Concluding the Presentation

Once discussion has concluded, whether naturally or you have had to bring the discussion to a close in order to complete the session within the time allowed, it is time to give the quiz (if you are using it). Again, remind the attendees that the quiz is only meant to help determine how effective the presentation of the information is, and that they will not be graded on it. Let them know that they have approximately five minutes to complete the quiz.

At the end of the five minute period, remind the attendees to date and sign their quizzes, and then collect them. The attendees should be thanked for attending the session and reminded of any other sessions in the educational program that they may be attending. They can then be dismissed to return to their normal activities.

*(An alternative to this approach is to give the quiz immediately after showing the program, then use a review of the quiz as a basis for your group discussion.)

"Wrapping Up" the Paperwork

Before much time has passed, and the subject matter is fresh in your mind, several areas of "paperwork" must be completed. First, check to make sure that all attendees signed the scheduling and attendance form. Next, make sure that you have a quiz from every attendee, dated and signed.

Also, depending upon what you have decided to do, a copy of the attendance sheet and the quiz for each attendee should be either filed in your files, or turned over to the attendee's department manager (or the personnel office) so that this paperwork can be included in their personnel file. The attendees' training logs should also be updated, and each attendee should be given a filled out and signed training certificate, signifying that they have successfully completed the course.

OUTLINE OF MAJOR PROGRAM POINTS

OUTLINE OF MAJOR PROGRAM POINTS

The following outline summarizes the major points of information presented in the program. The outline can be used to review the program before conducting a classroom session, as well as in preparing to lead a class discussion about the program.

Most of the time our days are spent with our feet firmly on the ground. At ground level, our tools and work surfaces are within easy reach.

But there are times when we need access to things that are more difficult to get to.

Sometimes a truck with a "lift bucket" can be brought in to raise us to the desired height.

For long-term projects, it may make sense to put up some scaffolding.

Most of the time though, working off the ground means bringing in a ladder.

When we use them correctly, ladders make our jobs easier, and make us more productive.

They allow us to work comfortably in places that are ordinarily out of our reach.

In fact, it's hard to imagine what we'd do without them.

But we've got to be careful, because whenever we're on a ladder there's always the possibility we could fall.

If they're used incorrectly, ladders can lead to accidents and serious injuries.

There are many different types of ladders. Each one is designed for a specific purpose.

They can all get you safely to the right height, providing you select the correct ladder for the job you're doing.

Straight ladders are often used to reach a roof or platform.

They should be tall enough so that the top three rungs of the ladder extend beyond the roof edge or support point.

This will keep the ladder stable while you're on it.

Sometimes an extension ladder may be what you need to get where you want to go.

To give you the proper support, there should be at least a three rung overlap between the two sections.

To determine how tall a ladder you need, follow the 4-to-1 ratio. Say you're putting a ladder against a wall.

The ladder should be about 1 foot away from the wall for every 4 feet of working ladder height.

If the ladder you've chosen can't maintain this ratio and reach your desired destination, you need a longer ladder.

You should also think about how much weight the ladder will have to hold.

Different ladders are built with different weight capacities.

Read the manufacturer's instructions to make sure the type of ladder you're using will support the weight you'll be putting on it.

Remember, to get a safe match you need to add the weight of the tools and materials that you'll be carrying to what the scale says you weigh.

Many accidents occur when workers fail to notice problems that have developed with their ladders.

Becoming familiar with the parts of the ladders that you use will help you to make sure they're in good condition.

For instance, rungs should be firm and unbroken.

To provide a stable base that prevents slipping, ladders should also have sturdy, non-slip safety feet.

Make sure that the ropes, pulleys and other moving parts on extension ladders are in good working order.

If you're using a stepladder, verify that the spreader is in good condition and can be locked into position before you climb.

Stepladders should also have braces to keep the rails and side supports from swaying.

Before climbing a ladder that is permanently fixed in place, make sure that:

All the rungs are securely attached.

There is no rust or corrosion on the safety cage or the rungs themselves.

As you inspect your ladder, fix or replace any damaged parts.

If you can't repair what's broken, talk to your supervisor, and get a new ladder!

Once you've selected the right ladder for the job, and inspected it, you need to set it up correctly.

First make sure to secure the legs.

Place them on a level surface, keeping the area around the base of the ladder clear of debris.

As you set the ladder up, be sure the rails are perpendicular to the ground.

This will help to ensure that the feet get positioned firmly.

If the ground is uneven, shore up the legs with wood, or ladder jacks.

If the ground is soft, placing wide boards under the feet of the ladder can help to keep it steady.

If you have to place a ladder in front of a door, block or lock the door so no one can come through it while you're working.

If you're using a straight or extension ladder, remember the 4-to-1 ratio.

Set the ladder up to be one foot "out" for every 4 feet of working ladder height.

This will keep the ladder at about a 75 degree angle, and make climbing safe and easy.

Most new ladders have a sticker that helps you to set them up with a 4-to-1 ratio.

Matching the angle of the ladder with the angle shown on the sticker will position the ladder correctly.

Try to get a "helper" to hold the ladder so it won't slip.

If no one is available, tie off the ladder at the top with a rope.

Remember, it's always a good idea to put hazard signs around the area where you're working.

One of the things that makes ladders so useful is that they can be moved to wherever we need them.

If possible, you should take the ladder down and carry it horizontally, at your side.

This will help you to keep your balance, and make the ladder easier to handle.

If you can't comfortably carry the ladder by yourself, don't risk an accident. Get help.

If you have to move a ladder while it's up, be very careful.

Make the move slowly.

It's easy for an extended ladder to throw you off balance or knock something down.

This is another situation where it's a good idea to have someone else give you a hand.

There are some situations when you shouldn't climb a ladder at all.

Don't climb a metal ladder if you're working near power lines, electrical wiring or machinery.

If a metal ladder comes in contact with an uninsulated power source, it will conduct the electricity straight to you!

If you're working around electricity, choose a non-conducting fiberglass or wooden ladder, to avoid the possibility of getting shocked.

Never climb ladders in poor weather conditions.

Rain and wind can make climbing dangerous.

Don't climb ladders if you're sick, or taking medication that makes you drowsy.

It's too easy to lose your balance if you're not feeling right.

Some people have a fear of being in high places.

Don't force or badger anyone into climbing a ladder, it could put both them, and you, at risk.

Once you've determined that your ladder is in good condition, and that the area you'll be working in is safe, read the manufacturer's instructions to determine if there are any special precautions you should take.

Then it's "time to climb".

First, get a good grip on the ladder.

Make sure that your shoes, hands and the rungs of the ladder are dry, and free of oil or other slippery substances.

When possible, use the "buddy system."

This is where a coworker holds the bottom of the ladder so it won't slip.

They'll also make sure that no one bumps into the ladder while you're working.

If you're alone on the job, tie the ladder off and set up "hazard signs" to keep people away from it.

When you're climbing follow the "3-Point Rule".

Keep two hands and a foot or one hand and two feet in contact with the ladder at all times.

Always face the front of the ladder, and never rush.

Keep your hands on the side rails, and don't try to slide down or jump off when you're finished.

To avoid falling accidents, you need to keep your weight centered between your ladder's rails.

Try using the "Belt Buckle Rule".

By keeping your belt buckle between the rails of the ladder at all times, you'll be sure to maintain your center of gravity.

You shouldn't lean out to the side or back when you're on a ladder either.

Stay close, so your weight is in line with the rails.

Standing too close to the top of a ladder is something else you should avoid.

It can cause you to lose your balance and hit the ground, hard!

In general, it's a good idea not to stand on the top 4 rungs of an extension ladder or the top 2 steps of a stepladder.

If you can't follow these guidelines with the ladder you have, get a bigger one.

Don't play games with your safety!

Never have more than one person on a ladder at a time.

Another person's movements can upset your balance.

The extra weight and stress can also weaken the ladder over time.

Stepladders are no exception.

Never let someone stand on the back of the ladder to help the person on the front, unless they're using a specially built "two person" ladder.

Hoisting tools or materials up with you while you're climbing can be very dangerous.

Instead, wear a tool belt, and pull up any other materials that you need after you've reached the top.

Fasten containers or tool holders to your ladder to hold things that you have to have quick access to.

They may not hurt you, but falling objects are dangerous to anyone below.

Watch out for people beneath you.

Be careful when you're handling your tools and materials.

Never leave a raised ladder unattended.

Once you're finished with it, store your ladder in a safe, dry place.

Sometimes, no matter how careful we are, things just go wrong.

If an accident does occur, it's important to be prepared.

If you do fall off a ladder, knowing how to fall "the right way" can prevent a serious injury.

Tense muscles increase the potential for getting hurt, so it's important to relax when you fall.

Absorb the concussion by bending your arms and legs.

This way they will act as "shock absorbers" when you hit the ground.

Rolling in the direction of the fall will "cushion" you even more.

If someone does fall from a ladder, they could end up with broken bones, a concussion or even damage to their spinal column.

Don't move them unless they are in a very dangerous location (movement will only make these injuries worse).

Instead, call for medical assistance immediately.

While you wait for help to arrive, monitor the victim's breathing and work to stop any bleeding.

In some cases, the victim may also need to be treated for shock.

*** SUMMARY ***

As we've seen, ladders can be a big help.

But they can also be dangerous if they're not used correctly.

Pick the right ladder for the job.

Make sure it's tall enough.

Check its weight capacity.

Inspect every ladder before you use it.

Take care of any needed repairs.

Set your ladder up on a firm, dry base, and make sure it's at the right angle.

Remember the "4-to-1" rule.

Climb with safety in mind. Secure the ladder firmly, and use the "3-point" climbing technique.

Stay inside the rails of your ladder at all times.

Never lean out or back at an angle.

If an accident does occur, be prepared to act.

Know what types of first aid may be needed.

Ladders can help us to be more efficient and productive. But if you don't use them correctly, you could find yourself "grounded", for a long time!

ACCOMPANYING MATERIALS

ACCOMPANYING MATERIALS

In order to assist you in conducting your session on ladder safety, we have provided some materials that can be used with this program. These materials have been furnished in "master" form. This will enable you to make as many copies of these forms as you need. If you have colored paper available to you, it is often useful to put each form on a different color. This enables you to easily differentiate between the materials. The materials enclosed with this guide include:

Scheduling and Attendance Form

This form is provided so you can easily schedule your attendees into each session of the program. It is important that you have each attendee "sign-in" on the appropriate form, documenting their attendance at the session. Normally, a copy of this attendance/"sign-in" form is filed in the employee's personnel file.

Quiz

The quiz is normally given after viewing the program. However, if you want an indication of the "increase" in the attendees' knowledge of ladder safety, you can give the quiz both before and after the program is shown. You can also use the quiz as the basis for class discussion. If you have decided to give the quiz both before and after the attendees view the program, it is often interesting to have the attendees compare their "before" and "after" answers as part of the session. Typically, the quiz is filed in the employee's personnel file.

Training Certificate

This form allows you to give each employee their own "certificate of completion" showing that they have attended the course and taken the quiz. Space is provided to insert the employee's name, the course instructor and the date of completion.

Employee Training Log

This log helps you to keep track of when each employee has taken the course, as well as associated courses/training. Space is provided to list pertinent data about the employee, as well as information such as the date the course was taken, and the instructor conducting the course. A copy of this form should be kept in each employee's training or personnel file.

Booklet*

A sample copy of the employee booklet that has been designed for use with this program has also been included. Using both text and illustrations to review important points, the booklet is designed to reinforce the message employees receive in the training session. The material is presented in the same order as seen in the program and is organized into concise sections, making it easy to understand and remember.

*Additional booklets, as well as copies of the poster that has been created to get employees thinking about ladder safety, are available from your distributor.